Specification

Product:		E-Z Arm Jr. - Lab & Bench Top to 6’ - Externally Supported - 2.5'' Ø (150 CFM) Extractor Arm

Application:		Extraction of fumes, dust, vapors, smoke or gases

Revision:		May 11, 2010

1.	E-Z Arm Jr. - Lab & Bench Top to 6’ - Externally Supported - 2.5'' Ø (150 CFM) (www.LEV-CO.com)

1.1.	General:

1.1.1.	The following extractor arms shall be of industrial quality, and be designed to be used for the extraction of fumes, dust, vapors, gases and smoke. They shall be manufactured to withstand the environments associated with these applications and when the appropriate local extraction devices are selected, these extractors shall remove the pollutants in accordance with all industrial ventilation guidelines.

1.2.	 Construction:

1.2.1.	Light weight and easily adjustable; designed for table top use to remove smoke, and fumes from the work area.

1.2.2.    Can be mounted directly to a small portable air cleaning unit.

1.2.3.    Complete with universal discharge (up, down, or through table) plenum assembly.

Arm assembly shall have 360° movements along its entire length.

1.2.4.    Two lengths are available 4Ft and 6Ft * long arm.

(*) All arm lengths refer to fully extended lengths.

1.2.5.    The tubes and hoods are white powder coat finish.

1.2.7.      The universal mounting bracket is designed to attach easily to the end of the workbench or to be wall 
               mounted, or to be mounted through a 3” hole in the workbench without field modifications.

1.3.	Specifications:

    - STD DIM:

|  | 2E04-DD | E-Z Arm Jr. 2.5” dia. extraction arm, 4’ long down-flange configuration. |  |  |
| --- | --- | --- | --- | --- |
|  | 2E04-FE | E-Z Arm Jr.. extraction arm, 4’ long up-flange configuration. |  |  |
|  | 2E06-FE | E-Z Arm ® 2.5" dia. 6' long, high performance, UP-FLANGE extractor with external support joint, flanged hood, white powder-coat aluminum tubes and hood, and white hose; includes universal mounting bracket with 3" dia. Outlet collar. (Order motor/blower assembly separately). |  |  |

1.3.2. Weight:	5 lbs for 4’ extractor arm

6 lbs for 6’ extractor arm

1.4.	Options:

    - Hose, hood options:

|  | 2AX0-2708 | Flanged hood, spun aluminum white powder-coat finish. |  |  |
| --- | --- | --- | --- | --- |
|  | 7HD5-0003 | Flex hose, white. (Old style, not self-supporting). Price is per foot. |  |  |
|  | E-Z ARM 2.5 | Light Kit 20 watt, 115V for use with Mini-Vac Arms.No Remote Switches Available). |  |  |

1.4.2. Accessories:

|  | 2E06 CS-1 | Ceiling/floor stanchion 1m (3.3') for EZ Arm Junior made of heavy gage material |  |  |
| --- | --- | --- | --- | --- |
|  | 2E06 CS-2 | Ceiling/floor stanchion 2m (7') for EZ Arm Junior made of heavy gage material |  |  |
|  | 2E06 CS-3 | Ceiling/floor stanchion 3m (10') for EZ Arm Junior made of heavy gage material |  |  |
|  | 7PH5-2008 | Rubber band. Clamp cover. White. (New Type). |  |  |
|  | E-Z ARM 2.5 | Air flow damper with ABS plastic baffle option for E-Z Arm 2.5 Arm. |  |  |
|  | SQ-BASE-PLATE-P-022 | Square base plate for ceiling/floor stanchion. |  |  |

1.5.	Performance ratings

1.5.1	See Spec Drawings for performance curves