Specification

Product:	200, 202 and 203 Dusts, Mists & Gases - Multiple filter configurations available - Washable and - or Disposable

filters - No Fan (1,000-2,000 CFM) (2,000-4,000 CFM) (3,000-6,000 CFM)

Application:	Dust, Mists Fumes and Gases. These units are blowerless filtration units designed with up to 4 stages of filtration for industrial applications.

Revision:		May 11, 2010

- Dusts, Mists & Gases - Multiple filter configurations available - Washable and - or Disposable

filters - No Fan (1,000-2,000 CFM) (2,000-4,000 CFM) (3,000-6,000 CFM) (www.LEV-CO.com)

1.1.	General:

1.1.1.	The following units shall be of industrial quality, and be designed to be used for filtration of dusts, mists and gases. They shall be manufactured to withstand the environments associated with these applications and when the appropriate local extraction devices are selected, these filters shall remove the pollutants in accordance with all industrial ventilation guidelines.

1.2.	 Construction:

    - All models use high efficiency particulate and gas filters and are completely non-electrostatic.

    - They are also ideal as an after filter for dust collectors, where higher efficiency is needed.

    - 16 gauge welded line coated steel cabinet, finished with a two part chemical and oil resistant paint,

with Ultra·Seal filter mounting system, and hinged side access doors to filters.

1.2.4.	 Blowerless construction.

1.3.	Specifications:

MODEL 200			MODEL 202			MODEL 203

1.3.1. DIMENSIONS:	 26” H x 24 1/2” W x 39 5/8” L	27 1/2" H x 48" W x 44” L		27 1/2" H x 44" W x 72” L

1.3.2. WEIGHT:		150 lbs.				250 lbs.				345Ibs.

1.4.	 Options

1.4.1. PREFILTERS:	4” Pleated std.			(2) 4” Pleated std.			(3) 4” Pleated std.

CHEVRON, opt.			(2) CHEVRON, opt.		(3) CHEVRON, opt.

Aluminum mesh, opt.		(2) Aluminum mesh, opt.		(3) Aluminum mesh, opt.

1.4.2. MAIN FILTERS:	120 sqFt multi·pocket		(2) 120 sqFt multi·pocket		(3) 120 sqFt multi·pocket

95% std., 65% opt.		(2) 95% std., 65% opt.		(3) 95% std., 65% opt.

Easy clean optional		(2) Easy clean optional		(3) Easy clean optional

1.4.3. AFTER FILTERS:	HEPA filter. 99.97%		(2) HEPA filter. 99.97%		(3) HEPA filter. 99.97%

with 66 SqFt multi·pocket. opt.	with 66 SqFt multi·pocket. opt.	with 66 SqFt multi·pocket. opt.

MODEL 200			MODEL 202			MODEL 203

1.4.4. AD OPTION:	(2) 25 lb. adsorber modules	(4) 25 lb. adsorber modules	(6) 25 lb. adsorber modules

Refillable. With 66 sqFT, 95%.	Refillable. With 66 sqFT, 95%.	Refillable. With 66 sqFT, 95%.

multi·pocket filter and 2" pleat	multi·pocket filter (2) and 2" pleat	multi·pocket filter (3) and 2" pleat

final filter, optional		final filter, optional		final filter, optional

1.4.5. OTHER OPTIONS:	 Pressure gauge kit indicates litter changes (Available for all models).

1.5.	Performance ratings

1.5.1	See Spec Drawings for performance curves