Specification

Product:		Direct drive fan

Application:		Extraction of fumes, dust, smoke or gases

Revision:		September 24, 2008

1.	Direct drive fans – LD Series (www.LEV-CO.com)

1.1.	General:

1.1.1.	The following direct drive fans shall be of industrial quality, and be designed to be used for the extraction of fumes, dust, gases and smoke. They shall be manufactured to withstand the environments associated with these applications and when the appropriate local extraction devices are selected, these extractors shall remove the pollutants in accordance with all industrial ventilation guidelines.

1.2.	Rotation and discharge positions:

1.2.1.	Four discharge positions and two rotations (CW or CCW) plus fans can be mounted horizontally (Maximum 600 pound motor)

1.2.2	Reversible housing provides increased configuration flexibility.

1.2.3	Removable side plates allow the wheel to be removed from the motor or inlet side of the housing.

1.2.4	Housings are rotatable in 45 degree increments.

1.3.	 Construction:

1.3.1.	Solidly built with continuously welded housings and mounting holes in all support flanges.

1.3.2.	Inlet collar for slip fit connection to the duct work

1.3.3.	Flanged outlet drilled with standard hole pattern

1.3.4.	¾” NPT, female pipe coupling with plug – as drain. Welded to lowest point on inlet side plate.

1.3.5.	Backward inclined blades are fabricated of heavy-gauge, high-strength steel

1.3.6.	Inlet side support is used to assure a vibration-free, stable housing

1.3.7.	Inlet bell is designed for smooth air entrance into the wheel inlet for maximum efficiency.

1.3.8.	Maximum temperature of standard design: 300°F. (149°C.); high temperature designs up to 750°F. (398°C.)

1.3.9	All fans are mechanically run tested prior to shipment to ensure the balance of the assembled unit.

1.4	Options:

1.4.1	Inspection door – Quick-release doors positioned as specified.

1.4.2	Spring Isolators

1.5.	Fan performance ratings

1.5.1	See Spec Drawings for fan curves