Specification

Product:		Direct drive fan

Application:		Extraction of fumes, dust, smoke or gases

Revision:		September 24, 2008

1.	Direct drive fans – P-MAX Series (www.LEV-CO.com)

1.1.	General:

1.1.1.	The following direct drive fans shall be of industrial quality, and be designed to be used for the extraction of fumes, dust, gases and smoke. They shall be manufactured to withstand the environments associated with these applications and when the appropriate local extraction devices are selected, these extractors shall remove the pollutants in accordance with all industrial ventilation guidelines.

1.2.	Rotation and discharge positions:

1.2.1.	Eight discharge positions plus fans can be mounted horizontally

1.2.2	Removable housing allows the wheel to be removed from the motor side of the housing.

1.2.3	Housings are rotatable in 22.5 degree increments.

1.3.	 Construction:

1.3.1.	Solidly built with welded housings and mounting holes in all support flanges.

1.3.2.	Inlet collar for slip fit connection to the duct work

1.3.3.	Flanged outlet

1.3.4.	Centrifugal wheel made from high-strength steel

1.3.5	Maximum temperature of standard design: 300°F. (149°C.); high temperature designs up to 750°F. (398°C.)

1.3.6	ll fans are mechanically run tested prior to shipment to ensure the balance of the assembled unit.

1.4	Options:

1.4.1	Wall/Ceiling/Floor Bracket

1.4.2	Spring Isolators

1.5.	Fan performance ratings

1.5.1	See Spec Drawings for fan curves