Specification

Product:	G-MAX-36 Extraction Crane

Application:	“At-source” extraction of fumes, dust, smoke or gases

Revision:	July 5, 2011

- G-MAX-36 Extractor Crane

  - General:

    - The following extractor cnanes shall be of industrial quality, and be designed to be used for the extraction of fumes, dust, mist, gases and smoke. They shall be manufactured to withstand the environments associated with these applications and when the appropriate fans are selected, these extractors shall remove the pollutants in accordance with all industrial ventilation guidelines.

    - The G-MAX-36 Extractor crane allows you to position the hose drop wherever required (in the limit of the coverage range) and to position the extraction system against the wall and out of the bay.

  - Coverage distance and operating temperature

    - The Extraction Crane will reach as far as 36 ft into the service bay and pass over the top of heavy equipment with ease. The integrated hose drop extends the reach ability with another approx 5 ft.

    - Low Temp. Hose: suitable for temperatures up to 250° F

    - High Temp. Hose: suitable for temperatures of 600° F

    - Very High Temp. Hose: suitable for temperatures of 1200° F

  - Construction:

    - All Systems consist of heavy wall bracket, 3 sections of articulated crane, complete with the following components:

      - Spiral duct with flexible hose at joints across the top of the boom;

      - Swivel to couple the extractor crane’s first hose section to the ductwork

      - Pneumatic blast gate to shut down at any time the extraction crane

      - End elbow and fixing bracket

      - Hose drop with balancer

  - Options:

    - Miscellaneous nozzles and / or hoods.

  - Exact positioning:

    - In addition to the extraction crane being able to be moved around with great ease, it shall also be provided with friction disks at each specified joint. This is to ensure the extraction crane can be moved to any position in it's range of movement and put in place without "Drifting" away from the point of extraction.

  - Hardware:

    - The extraction crane shall be supplied with all necessary hardware required for assembly and duct connection. Hardware for mounting the extractor to the wall or column is to be provided by the installing contractor or end user.

  - Acceptable Product:

    - “G-MAX-36” extraction cranes manufactured by LEV-CO.

    - Toll Free:  (888)-862-5356

    - Website & Email: www.LEV-CO.com    /    Sales@LEV-CO.com